## Slide 1: Compiling Resource-Efficient Programs with BQSKit
Ed Younis, Justin Kalloor, Mathias Weiden, Siyuan Niu, Costin Iancu

## Slide 2: Quantum Hardware R&D is Experiencing a Boon
Extremely diverse hardware landscape
Steady stream of new gates, architectures, and constraints
Increases burden on the software stacks and compilers
Compilation has many different meanings
  High Level to Circuit Program Generators
  Circuit Transpilers (optimizers, constraint solving)
  Control level compilation (circuit to control signals, hardware specific languages, etc)
Google IBM Intel IonQ Rigetti

## Slide 3: Berkeley Quantum Synthesis Toolkit (BQSKit) [bis • kit]
Gracefully handles every gate set and architecture
Specialized pipelines for widely-used chips
Generates resource efficient circuits (width, depth, timing, etc)
Error mitigation
Enables effective algorithm and hardware design exploration
20+ papers (3 IEEE QCE best papers: 2020, 2021, 2022)
500K+ downloads
Powerful and Portable Quantum Compiler Framework
LANL
Sandia
ANL
ORNL
LLNL
U Penn
U Del
U Chicago
U Kansas
U Tokyo
NCSU
Duke
CUNY
U Wisc
Quantinuum
Infleqtion
AWS
Microsoft
NVIDIA
UnitaryFund
HSBC
bqskit.lbl.gov
Users:

## Slide 4: Turn-key Functionality that Works Everywhere
Python 3.9+ on Windows, Mac, Linux
(from laptop to supercomputer)
Any gate set or architecture in or out
qubits, qudits, states, many-states, unitaries, and more
(from experiment to real hardware)

## Slide 5: Parameterized Circuit Instantiation: A Powerful Primitive
Parameterized Circuit Instantiation
Given a parameterized quantum circuit and a target unitary , solve for
Parameterized Circuit
Instantiated Circuit

## Slide 6: Instantiation Enables Function and Structure Separation
Can isolate and vary circuit function and structure
Instantiated Circuit
Instantiated Circuit
Parameterized Circuit
Structure
Mathematical Representations
Function

## Slide 7: Instantiation is the Core of Bottom-Up Synthesis
The standard bottom-up loop is to create an initial circuit template guess then continue to instantiate and extend it until a solution is found
Circuit
Unitary
E. Younis et al., “QFast: Conflating Search and Numerical Optimization for Scalable Quantum Circuit Synthesis.” 2021 IEEE International Conference on Quantum Computing and Engineering (QCE). IEEE, 2021. (Best Paper Award)

## Slide 8: Instantiation-Based Circuit Transformation Flow
We have found Instantiation can also be used to transform or optimize a quantum circuit. Instead of extending a circuit template like in bottom-up synthesis, we reduce or transform a circuit template and continue until it is no longer successful or necessary.
E. Younis et al., “Quantum Circuit Optimization and Transpilation via Parameterized Circuit Instantiation.” 2022 IEEE International Conference on Quantum Computing and Engineering (QCE). IEEE, 2022

## Slide 9: Gate Deletion is Straight Forward with Instantiation
Suboptimal circuits can have gates removed and others reinstantiated to accommodate the loss
Gate deletion + Candidate selection = Optimization algorithm
Extremely portable and flexible
Very effective due to global transformations

## Slide 10: Instantiation-Based Algorithms in BQSKit
QSweep – 1 qudit, pulse-optimal
QSearch – 2-4 qudits, optimal
ACDC – Dynamic Circuits
PAS – 3-4 qudits, better-than-optimal + post-processing
LEAP – 4-6 qudits
QFAST – 5-8 qudits
QPredict – 6-12 qudits
Retargeting
Gate Deletion
Template Substitution
Circuit Resizing
Circuit Synthesis
Instantiation
Circuit Transformation

## Slide 11: Partitioning Scales Instantiation to 1000s of qubits
Circuit on the left is partitioned into 3-qubit blocks below
Partitioning overcomes the exponential scaling of numerical instantiation
Restricts global view; can adjust block size for better performance or quality
Creates an extremely parallel workflow
X.C. Wu et al. “Reoptimization of Quantum Circuits via Hierarchical Synthesis.” 2021 IEEE International Conference on Rebooting Computing (ICRC). IEEE, 2021.

## Slide 12: Push-button Compiler Verification
Small circuits can have their error directly calculated
Larger circuits can be first partitioned into large simulatable sections, then summing the section errors gives an upper bound on total error
Unless specified, we target 10-8 to 10-10 instantiation verification error, most often it is less

## Slide 13: Instantiation-Based Workflows in BQSKit
PAM maps circuits with fewer final gates than commercial compilers
Workflows perform end-to-end compilation tasks:
  Resource Optimization
  Mapping/Routing
  Transpilation
  Error Mitigation
  Fault Tolerant Compilation
  Design Exploration
Advanced capabilities in BQSKit:
  Dynamic Circuit Synthesis
  Performance and Quality Scaling
  Hardware Portability
  Circuit Approximations
Workflows can be composed to produce pipelines

## Slide 14: Berkeley Quantum Synthesis Toolkit Tutorial
github.com/bqskit/bqskit-tutorial
qce25 branch